## Slide 1
JAIPUR HOSPITAL ENERGY RESILIENCE
Test tomorrow
before it arrives.
A reproducible digital twin that explains critical failures and proves the smallest intervention on unseen futures.
500 futures, 288 intervals each, same-seed proof
GROUNDED / SUB-FIVE-MINUTE JUDGE PITCH
Notes: Timing: 0:00–0:30
Climate resilience is usually tested after the emergency. Grounded lets a hospital test tomorrow before it arrives. It runs the energy system through hundreds of reproducible heat, cloud, demand and outage futures, explains the exact chain behind every critical failure, and proves the smallest operating change on futures the optimizer never saw.
Sources:
- Grounded Engine 2.5 verified public build

## Slide 2
A REAL JAIPUR ANCHOR
The intervention exists. Outage proof still needs telemetry.
02
70 kWp
ON-GRID SOLAR
≈80%
REPORTED DEMAND SHARE
Rajkiya Dharamshala, Sawai Man Singh Hospital
2025-26 field-assessed case, Jaipur, Rajasthan
WHAT THE SOURCE PROVES
Real facility, documented solar intervention
Operational interviews, material reported bill reduction
Chart: 
| Before | After
Monthly electricity bill (₹) | 90000 | 40000
reported monthly bill
BOUNDARY No 15-minute meter, inverter or outage telemetry is published.
Source: Aavas Foundation / SGS impact assessment, pp. 9, 17, 22
Notes: Timing: 0:30–1:10
This is not a fictional Jaipur problem. A published 2025–26 impact assessment documents a 70-kWp solar plant at Rajkiya Dharamshala, SMS Hospital. A hospital representative reported roughly 80 percent demand coverage and a monthly bill reduction from about ninety thousand to forty thousand rupees. That establishes a real facility and intervention. It does not provide 15-minute meters or prove islanded outage performance—and Grounded says that openly.
Sources:
- https://www.aavas.in/img/pdf/solar-power-plants-in-government-hospitals-2025-26.pdf — pages 9, 17, 22

## Slide 3
FROM SOURCE TO DECISION
One facility becomes 500 exact operating futures.
03
01
OBSERVE
Jaipur climate
Measured operational reference
02
DISPATCH
Solar supports critical load
Grid and battery cover flexible load
03
STRESS
Heat + cloud + demand + outage
288 × 15-minute timesteps
04
PROVE
Same seed before / after
Holdouts + assumption shocks
RUNS LOCALLY IN THE PUBLIC BROWSER
Disclosed reference: Ausgrid demand + PV + 9,210 outage/restoration records
Notes: Timing: 1:10–1:50
Grounded combines Jaipur NASA POWER climate observations with a disclosed, measured Ausgrid operational reference: quarter-hour demand, measured PV and 9,210 outage/restoration records. It dispatches solar, grid and battery through 288 15-minute intervals for each future. Every run is deterministic, every source is fingerprinted, and the public site executes the engine in the browser, so judging does not depend on a fragile backend.
Sources:
- https://power.larc.nasa.gov/docs/services/api/temporal/hourly/
- https://www.ausgrid.com.au/about-us/about-ausgrid/research-data-sets/distribution-zone-substation-data
- https://data.gov.au/data/dataset/solar-home-electricity-data
- https://data.peclet.com.au/explore/dataset/ausgrid-past-outages/table/

## Slide 4
RISK EVIDENCE
The baseline fails in 15 futures. Grounded explains every one.
04
3.0%
critical-loss risk
15 / 500 futures
95% CI, 1.8 to 4.9%
CAUSAL CHAIN
01 Demand surges
02 Heat spikes
03 Cloud cover
04 Grid lost
05 Battery 10%
06 Hospital unserved
7/7
PHYSICS INVARIANTS
1.14e−13
MAX BALANCE ERROR KWH
1.000
ML HOLDOUT AUROC
0.008
BRIER SCORE
2.3%
CALIBRATION ERROR
The ML surrogate explains simulator behavior; it never controls dispatch or the recommendation.
Notes: Timing: 1:50–2:40
In the extreme run, 15 of 500 futures lose hospital power: 3.0 percent, with a 95 percent interval of 1.8 to 4.9. Grounded does not stop at that percentage. It shows the first loss timestamp, energy balance, LOLP, LOLE, EENS, CVaR tail risk and the full causal chain. A compact held-out ML surrogate reaches 1.000 AUROC, but it is diagnostic only. Exact physics remains the authority, and seven of seven machine invariants pass.
Sources:
- Grounded Engine 2.5 deterministic run on measured operational reference
- Run fingerprint in verified public-build rehearsal: GRD-9C1ED390

## Slide 5
DECISION PROOF
The smallest policy survives what the optimizer never saw.
05
Chart: 
| Current plan | Grounded policy
Critical failures | 15 | 0
same original 500 futures
20% reserve, 180m EV delay, pre-cool 11:00
245
STRATEGIES SEARCHED
5
HAZARDS
300
SEARCH FUTURES
3/3
DISJOINT HOLDOUTS
4/4
ASSUMPTION SHOCKS
7 to 0
HOLDOUT FAILURES
0 introduced regressions, 11/12 observed climate stress periods passed
Notes: Timing: 2:40–3:30
Grounded exhaustively searches 245 reserve, EV-delay and pre-cooling policies across five hazards on an independent 300-future cohort. The selected policy—20 percent reserve, 180-minute EV delay and 11 a.m. pre-cooling—takes the original 500-future baseline from 15 critical failures to zero. It then passes three disjoint holdouts, four assumption shocks, and prevents seven holdout failures without introducing one. Same seeds before and after mean the policy cannot win by getting an easier scenario.
Sources:
- Grounded Engine 2.5 verified static-browser optimizer rehearsal
- Proof run fingerprint: GRD-697CA17E

## Slide 6
REAL-WORLD PATHWAY
Credibility grows step by step.
06
01
PUBLISHED EVIDENCE
Named Jaipur facility + field-assessed solar case
02
OUTREACH READY
Minimum data contract + reviewer packet prepared
03
REPLY
RECEIVED
Named hospital / foundation reviewer replies
04
DATA GRANTED
30 days demand + PV + outage exports
05
COMMISSIONED
Quality-gated Jaipur site fingerprint
CURRENT TRUTH
No partnership is claimed yet. Next proof: a named reviewer reply.
Priority collaborators: SMS Hospital operations / CMO office, Aavas Foundation, Gram Bharati Samiti
Notes: Timing: 3:30–4:05
We are at the public-evidence and outreach-ready stage. We have a named Jaipur facility, a source-checked field assessment, a minimum data contract and a review packet for the hospital operations team and Aavas Foundation. We do not claim a partnership before someone replies. The next evidence step is a named reviewer and permission for 30 days of 15-minute demand, PV and outage data; then Grounded quality-gates and fingerprints a commissioned site twin.
Sources:
- https://www.aavas.in/contact-us
- https://rajswasthya.rajasthan.gov.in/contact.php
- https://gbsjaipur.org/about/
- D:/Grounded/docs/JAIPUR_FIELD_PARTNERSHIP.md

## Slide 7
THE ASK
Make Jaipur’s
next outage boring.
20-minute technical review
+ 30 days of demand, PV and outage exports
PUBLIC DEMO
grounded-peach.vercel.app
Reproducible engine, source-checked Jaipur case, commissioning-ready contract
Notes: Timing: 4:05–4:25
The public demo is live and reproducible. Our ask is small: a 20-minute technical review and three non-sensitive exports covering 30 days. Give Grounded one real boundary and one real outage history, and we will turn resilience from a promise into a test. Make Jaipur’s next outage boring.
Sources:
- https://grounded-peach.vercel.app
- D:/Grounded/data/SITE_DATA_CONTRACT.md